## Slide 2
Maintenance
Achievement
Program
Anita Bush, P.E., CPM – Chief MAM Engineer
Maintenance and Asset Management Division
1301 Old Hot Springs Road
Carson City, NV 89706
Main No. (775)-888-7487

## Slide 3: Agenda
Review scope and approach
Data Collection Methods
Deliverables
  Web Mapping Application (Deficiencies)
  LOS Scorecards
Quality Assurance/Control
Proposed MAP Manual Updates

## Slide 4: Project Scope
The Maintenance Achievement Program (MAP) is an initiative that aims to objectively measure the Level of Service (LOS) provided by NDOT highway maintenance tasks.

## Slide 5: Project Scope Cont.
LOS data is collected statewide and compared to established targets for each maintenance task, allowing NDOT to more effectively plan, budget and manage highway maintenance work.

## Slide 6: Project Approach
Conduct comprehensive training and field exercises with NDOT Maintenance and Asset Management staff and our in-house Data Collection team
Collect LOS data for a representative sample of Nevada highway system using strictly controlled data collection methods

## Slide 7: Data Collection Methods
Field surveys are performed at statistically valid, 0.10 mile (528’) randomly chosen segments across the Nevada state highway system.
Field data collection is performed using ArcGIS Collector and Survey123 applications on mobile devices

## Slide 8: Old Data Collection Method
Paper Forms
  Lost, misplaced, damaged or filled out incorrectly
Field Data transferred to database
  Transcription Errors
Multiple Collection Teams
  Evaluates Asset Deficiencies Differently
Photos of Deficiencies
  Lost, misplaced or labeled wrong

## Slide 9: New Data Collection Method
1,100 Random 528’ segments created from Python script running in ESRI’s ArcGIS software. (1,000 required, extra 100 allow for survey skips due to construction or safety issues).
Hosted Feature Class (ArcGIS Pro) is created through ArcGIS Online (AGOL)
Web Map created in AGOL using hosted feature service.
Collector for ArcGIS (iOS, Windows or Android operating systems) uses Web Map (map centric).
M.A.P. Survey created in ArcGIS Survey123 (form centric).
Collector and Survey123 are downloaded on handheld PDA device (iPad Pro, iPhone).
Surveys are completed electronically in the field and all pictures of deficiencies and other issues are attached directly to the survey, with geotag.
ArcGIS Dashboard is created from data to summarize task totals for the entire state.
Once data collection is complete, data is exported from AGOL and LOS’s are calculated for each task by district.

## Slide 10: ArcGIS Collector
Web Map contains survey segments and reference layers to assist in surveys, (Right-of-Way, Pipes, Mile Markers, etc.)
Map layers can be toggled on/off

## Slide 11: ArcGIS Collector cont.
Survey Sample is located and relevant attributes are displayed in the Details pane.
Attribute for Survey Status is edited in Collector
  Not Surveyed
  Skipped Survey
  Shifted Survey
  Survey Completed
Link to Survey123 is located in Collector app

## Slide 12: ArcGIS Survey123
Survey ID, Location, Date and Time are automictically populated in ArcGIS Survey123 from ArcGIS Collector

## Slide 13: ArcGIS Survey123 cont.
All tasks are separated into functional groups which can then be expanded to collect individual task data

## Slide 14: ArcGIS Survey123 cont.
Replace unreliable paper-based data collection with a trustworthy digital solution
Attach photographs to surveys
Add text descriptions to surveys, describing deficient assets

## Slide 15: ArcGIS Dashboard
Data from Survey123 is displayed real time in a configurable Dashboard.
Blue Oval – Functional Groups
Red Oval – Separate Tabs for Individual Tasks
NDOT Dashboard

## Slide 16: ArcGIS Online
Ability to show all deficiencies
Ability to filter results by District and Task
Easy to share with entire Department
All survey data available to viewers

## Slide 17: Statewide Scorecard

## Slide 18
District 1 Scorecard

## Slide 19: District 2 Scorecard

## Slide 20
District 3 Scorecard

## Slide 21: Quality Assurance/Quality Control
Maintenance and Asset Management HQ Staff performs QA/QC field reviews
NDOT conducted field QA trips in Las Vegas, Elko, and Reno/Carson City areas shortly after initial field data collection
QA/QC team worked from a random subset of sample sites
QA/QC team reviewed completed Data Collection Reports for accuracy and precision within acceptable tolerance

## Slide 22: Proposed MAP Manual Updates
Each year, our team will evaluate the data, the collection process, and the documentation to ensure that we maintain excellence and accuracy with our MAP Program

## Slide 23: Questions?