## Slide 1: Maintenance Peer Exchange NCHRP Project No. 20-68A Domestic Scan 14-01 Leading Management Practices for Determining Funding Levels for Maintenance and Preservation September 18, 2018
Rudy Powell
Florida Department of Transportation
Director, Office of Maintenance

## Slide 2: Selecting Performance Measures and Setting Performance Targets
Road Map
Section 334.046(4)(a), Florida Statutes
The Maintenance Rating Program
Discussion Questions

## Slide 3: Section 334.046(4)(a), Florida Statutes
This statute establishes preservation as a prevailing principle of the Department.
This "preservation first" requirement defines performance measures and targets for pavements, bridges, and roadway maintenance.
For roadway maintenance, the statute requires the Department to achieve 100% (target) of the acceptable maintenance standard (measure) on the state highway system. What is the acceptable maintenance standard?
The Department’s Maintenance Rating Program (MRP) defines the acceptable maintenance standard.

## Slide 4: The Maintenance Rating Program (MRP)
The MRP is a uniform, systematic, sample based evaluation system that consists of three primary components- Field Assessments, Administration, and Quality Control/ Quality Assurance Reviews.
Selecting Performance Measures. The MRP Handbook defines the desired maintenance conditions or performance measures.
Setting Performance Targets. The Roadway and Roadside Maintenance Procedure defines the acceptable maintenance standards or targets.

## Slide 5: Selecting Performance Measures The MRP Handbook
The MRP divides the state highway system into:
    four facility types (urban limited access, urban arterial, rural limited access, and rural arterial)
    five elements (roadway, roadside, traffic services, drainage, and vegetation/ aesthetics)
    35 characteristics which are unique features of individual elements (e.g. unpaved shoulder, front slope, sidewalk, slope roadside mowing, litter removal, etc.).
The desired maintenance conditions or performance measures are specified in the MRP Handbook for each characteristic.

## Slide 6: Selecting Performance Measures The MRP Handbook
A field assessment is performed comparing the actual maintenance conditions to the desired maintenance conditions using a meet/ does not meet criteria.
The meet/ does not meet assessment is compiled into a numeric score from 0 to 100 at the characteristic level, element level, and overall level.

## Slide 7: Selecting Performance Measures The MRP Handbook

## Slide 8: Selecting Performance Measures The MRP Handbook

## Slide 9: Setting Performance Targets The Roadway and Roadside Maintenance Procedure
The Roadway and Roadside Maintenance Procedure defines the district annual acceptable maintenance standard to be a MRP score of 80 overall, 75 at the element level, and 70 at the characteristic level.

## Slide 10: Discussion Questions
Do you adjust your targets based on the amount of funding available each year?
No. The Department does not adjust the targets based on the amount of funding available. Section 334.046(4)(a), Florida Statutes, establishes a "preservation first" requirement which means maintenance is funded “off the top” or before other programs. The Department uses the MRP scores or performance results to justify the maintenance funding request- accountability measure.

## Slide 11
Are separate targets established for districts?
No. The same performance measures and targets are used for all districts.
Are field personnel held accountable for meeting targets?
Not field personnel directly. District Secretaries, District Directors, District Maintenance Engineers, and District Operations Engineers are held accountable for meeting targets. MRP Specialists, Team Leaders, and Technicians are held accountable for meeting MRP quality control/ quality assurance reviews.

## Slide 12
What could be done better to make performance measures and targets more meaningful in your agency?
There must be confidence in the data. The maintenance rating program should be a uniform, systematic program with feedback loops and checks and balances to ensure the validity, applicability, reliability, consistency, and integrity of the program. This is critical when using the results for accountability or to justify needed funding.

## Slide 13
Questions?