## Slide 1: NCHRP 20-44 (005) Maintenance Peer Exchange Jerry Hatcher, P.E. Director of Maintenance
September 19, 2018

## Slide 2
ABOUT TENNESSEE

## Slide 3: Tennessee Highway System
Total Public Roads
Centerline Miles 95,523 mi
Public Bridges 19,823
Total State Roads
Centerline Miles 13,884 mi
Lane miles 37,447 mi
State Bridges 8,386
Interstate CL Miles 1,181 mi
Notes: Tennessee has a total 95,523 miles (153,725 km) of public roads. These include everything from rural gravel roads and city streets in subdivisions to main arterial highways.
TDOT is responsible for the 13,884 miles (22,344 km) of the heavier traveled state highway network. When you account for all of the lanes of these roads, we are responsible for 37,447 miles (30,263 km) of travelled lanes.
Of this state maintained network, 1,104 miles (1,777 km) are our interstate highways, our primary freeway network. While they only comprise about 1.2% of the road network in Tennessee they carry 27% of all traffic volume.
Our highway system also include support facilities such as our Traffic Management Centers in the four largest cities along with their ITS infrastructure, 14 Welcome Centers supporting tourist development, 18 motorist Rest Areas, and 10 Truck Weigh Stations for commercial vehicle enforcement activities.

## Slide 4
ABOUT
TDOT

## Slide 5: TDOT Size & Organization
4 Regions 3,900 Employees
12 Districts 1,400 Field Maintenance
95 Counties

## Slide 6
HIGHWAY
REVENUE

## Slide 7: 2017 IMPROVE Act
- Effective July 1, 2017
- First fuel tax increase since 1989.
- Gasoline tax raised from 20 cents to 26 cents over three years.
  Not indexed
- Diesel tax raised from 17 cents to 27 cents over three years.
  Not indexed
- New electric vehicle registration fee of $100 per year. Other vehicle registration fees increased.
- Provides funding for 962 projects in all 95 counties with an estimated cost of $10.5 billion.
  Will take about 14 years to have all projects under contract.

## Slide 8: TDOT Revenue Sources
Chart: 
| State | Federal | Local
Budget FY 2015 | 1036 | 996 | 42

## Slide 9: TDOT Revenue Sources

## Slide 10: TDOT Revenue Sources

## Slide 11: No TRANSPORTATION debt
TN
Notes: While we are nationally recognized for our transportation and the maintenance of our whole system, we are able to do that w/o transportation debt
We are only one of five states in nation with no transportation debt
2010 Tennessee spent - LOWEST OF 50 STATES
HIGHEST Good Roads & Bridge Conditions
No transportation Debt
Pay as you go

## Slide 12: Per Capita Revenue Used for Highways
Source: Federal Highway Administration
Dollars
$700 Nat’l Avg
$326
Lowest Per Capita Revenue in the Nation
$326
2017
Year of the last revision to the state gas tax in TN
26.4¢/gal Gas Tax
18.4¢/gal
Diesel Tax

## Slide 13: Setting the Stage Tennessee’s Current Outlook
Funding Outlook
Current revenues are not keeping up with growth
Notes: Lot of good things happening, but not sustainable
Current Revenues are not keeping up with growth (population and employment growth)
Funding Outlook
Demand exceeds long term funding
Inflation and project costs outpacing available revenues
No change in state fuel taxes or transportation revenues since 1989
Increasingly difficult to cover non-federal match amounts on federal funds to the State

## Slide 14: Fuel Efficiency – A Challenge
GAS TAX PAID PER NEW VEHICLE**
**Assumes 15K Miles/Year for a new vehicle Source: US DOT
28 MPG
36 MPG
54.5 MPG
$213/year
$166/year
$107/year
1990
2013
2025
Average mpg for light duty vehicles in new model year US fleet
Average mpg for light duty vehicles in new model year US fleet
CAFE Standard for 2025 model year US fleet
Notes: In 1990, if you purchased new car, it got 28 mpg and you paid ~$213 in gas tax
In 2013, the avg new car got 36 mpg and you were only paying ~$166 in gas tax
In 2025, when the CAFÉ standards are implemented, a new vehicle will get 54.5 mpg, which further decreases gas tax
Corporate Average Fuel Economy (CAFE) Standards for 2025
The first two MPG's is the national average of new vehicles in the years depicted. The last one described is correct as the federally mandated CAFÉ rules.

## Slide 15: Maintaining Our Assets
Chart: Interstate Pavement Condition
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Very Poor | 0 | 0 | 0 | 0 | 1.23 | 4.93 | 7.33 | 8.11 | 9.17 | 13.98
Poor | 0 | 2.03 | 2.15 | 4.5 | 6.24 | 5.28 | 6.23 | 6.94 | 8.93 | 10.78
Fair | 100.68 | 149.13 | 219.03 | 257.67 | 344.57 | 431.51 | 533.69 | 824.46 | 900.37 | 894.16
Good | 1662.34 | 1865 | 1719.55 | 1560.18 | 1319.47 | 1076.89 | 918.66 | 714.78 | 771.3 | 877.51
Very Good | 446.53 | 193.39 | 268.82 | 387.2 | 538.04 | 690.94 | 743.64 | 655.26 | 519.78 | 413.12
In 2015, 95.4% of Tennessee’s interstate pavements are in good or very good condition.
At current funding levels, by 2024, only 59.4% of interstate pavements will be good or better.
Source: FHWA
Notes: Our pavements, bridges, and other pieces of our highway network are in top quality condition.
As this slide shows, our Interstates are in great condition today, but even with long term funding at current levels, the quality of our Interstate pavements will drop nearly in half over the next 10 years.
Similar data is available for our non-interstate pavements, bridges, signing, and other infrastructure components.
An ageing infrastructure and the effects on inflation of stagnate transportation revenue will have a significant impact on the quality of these assets over time.

## Slide 16
HIGHWAY
BUDGET

## Slide 17: How We Spend Our Money
Chart: 
| Construction Projects | Maintenance & Preservation | Grants | Field Operations | Equipment & Facility | Other State Agencies | Administration | Other
FY 2014 | 0.63 | 0.18 | 0.09 | 0.03 | 0.02 | 0.02 | 0.02 | 0.01

## Slide 18: How We Spend Our Money
Maintenance & Preservation
18% of TDOT’s Budget
Chart: 
| Construction Projects | Maintenance & Preservation | Grants | Field Operations | Equipment & Facility | Other State Agencies | Administration | Other
FY 2014 | 0.63 | 0.18 | 0.09 | 0.03 | 0.02 | 0.02 | 0.02 | 0.01

## Slide 19: Maintenance & Preservation Budget Breakdown
Chart: 
| Routine Maintenance | Contract Maintenance | Resurfacing | Bridge Repair | Other
451 Budget Breakdown | 123696865 | 83217135 | 45000000 | 37945000 | 12400000
FY 2018
$312,423,900
Chart: 
| Construction Projects | Maintenance & Preservation | Grants | Field Operations | Equipment & Facility | Other State Agencies | Administration | Other
FY 2014 | 0.63 | 0.18 | 0.09 | 0.03 | 0.02 | 0.02 | 0.02 | 0.01
15%
100% State Funding
Additional Federal Funding
Resurfacing ($182 M)
Bridge Replacement ($105 M)

## Slide 20: Bridge Preservation Budget FY 2018
Program | Funds (Millions)
Bridge Replacement - Federal NHPP | $37.0
Bridge Replacement - Federal STP | $30.0
Bridge Repair - State | $37.0
Bridge Preservation | $4.4
Bridge/Tunnel Inspection – Federal HSIP | $8.0
Total | $116.4
Chart: 
| Routine Maintenance | Contract Maintenance | Resurfacing | Bridge Repair | Litter Pickup | Hwy Beautification | Env Compliance
451 Budget Breakdown | 123696865 | 83217135 | 45000000 | 37945000 | 6200000 | 1200000 | 5000000
Bridge Repair

## Slide 21: Pavement Preservation Budget FY 2018
Program | Funds (Millions)
Interstate – Federal NHPP | $66.0
NHS Routes– Federal NHPP | $55.0
State Routes – STP Federal | $61.0
State Routes – State | $45.0
Total | $227.0
Chart: 
| Routine Maintenance | Contract Maintenance | Resurfacing | Bridge Repair | Litter Pickup | Hwy Beautification | Env Compliance
451 Budget Breakdown | 123696865 | 83217135 | 45000000 | 37945000 | 6200000 | 1200000 | 5000000
Resurfacing

## Slide 22: Highway Maintenance FY-18 Budget
Program | Funds (Millions)
In-House Routine Maintenance | $125.7 (60.5%)
Contract Maintenance | $82.0 (39.5%)
Total | $207.7
Chart: 
| Routine Maintenance | Contract Maintenance | Resurfacing | Bridge Repair | Litter Pickup | Hwy Beautification | Env Compliance
451 Budget Breakdown | 123696865 | 83217135 | 45000000 | 37945000 | 6200000 | 1200000 | 5000000
Routine Maint.
Contract Maint.

## Slide 23: Winter Maintenance Budget History
FISCAL YR | STATEWIDE BUDGET | STATEWIDE EXPENDITURES
13-14 | $19,755,629 | $21,008,522
12-13 | $19,759,705 | $13,299,472
11-12 | $15,554,993 | $7,199,022
10-11 | $14,743,750 | $28,926,453
09-10 | $12,005,458 | $23,668,214
08-09 | $10,226,229 | $11,362,178
07-08 | $12,642,035 | $9,742,637

## Slide 24
BRIDGE MANAGEMENT

## Slide 25
Bridge Management
  Bridge Inspections performed by Regional Inspection Teams
  Bridge Evaluation and Design performed by HQ Structures Division
  Minor repairs by Regions, Major Repairs/Replacements by contract
Who is Involved?
How are Funds Allocated to Regions/Districts?
  HQ Prioritizes Bridges for Replacement/Rehab/Repair

## Slide 26
Bridge Management
  Bridge Program is optimized to replace more deficient deck area than is expected to be added each year based on NBI data
  % Bridge Deck Structurally Deficient
How is the Program Optimized?
Performance Measures

## Slide 27
Chart: 
| 2002-03 | 2003-04 | 2004-05 | 2005-06 | 2006-07 | 2007-08 | 2008-09 | 2009-10 | 2010-11 | 2011-12 | 2012-13
Structurally Deficient Deck Area Added, SqFt | 548051 | 900813 | 889416 | 682640 | 368429 | 602783 | 345526 | 701883 | 548009 | 345526 | 700100
Structurally Deficient Deck Area Removed, SqFt | 666119 | 988630 | 1120812 | 1264756 | 640848 | 660281 | 945928 | 327143 | 405556 | 945928 | 785851
Bridge Management – Optimization
Square feet
5 Year Average
~150,000 SqFt
More Deficient Deck Area Removed from System than Added

## Slide 28: Bridge Performance Measurement
Chart: % of Deck Area Structurally Deficient
| 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Structurally Deficient | 0.13713 | 0.11869 | 0.081016 | 0.072037 | 0.066403 | 0.066433 | 0.073146 | 0.066829 | 0.059563 | 0.060025 | 0.060484 | 0.058082 | 0.051883 | 0.045783 | 0.040624 | 0.041208 | 0.042123 | 0.039419 | 0.0406 | 0.041192 | 0.036237 | 0.034194
Notes: we are projecting the number to drop to around 2% by 2017.

## Slide 29
Bridge Management
  Large bridges (>20,000 sq.ft.) can be “budget busters”
  Federal funding future is unknown
  State funding levels have been flat
  Not able to forecast bridge condition for given funding scenarios
  Separate line item in budget for large bridges
  Using Bridge Management System that has forecasting capability.
Challenges
Recent Changes

## Slide 30
PAVEMENT MANAGEMENT

## Slide 31
Pavement Management
  Data collection/analysis at HQ
  PMS Data shared with Regions/Districts
  Project Selection by Regions/Districts
  Project Approval by Executive Leadership
  By % of Lane Miles
Who is Involved?
How are Funds Allocated to Regions/Districts?

## Slide 32
Pavement Management
  Pavement Management System
  Remaining Service Life – Lane Mile Years
  Interstate System is Highest Priority
  Regions/Districts Select Proper Treatments Locally
  Approximate 10% to 25% of treatments are preservation
  Pavement Quality Index (PQI)
How is the Program Optimized?
Performance Measures

## Slide 33: Freight Tonnage 2007

## Slide 34: Freight Tonnage 2040

## Slide 35: What you need to have a successful Pavement Preservation Program
Properly identify pavement deficiencies
Apply the appropriate treatment to the roadway
Know your network weaknesses
Have competent personnel making decisions
Verify what you do is working

## Slide 36: Pavement Management System
3 Major Components | TDOT’s Solution
System for Collecting Data | Mandli Communications – Distress, IRI, and Rutting
Database to sort and store Data | Stantec’s Highway Pavement Management Application (HPMA)
An analysis program to evaluate repair or preservation strategies, and suggest cost-effective projects for maintaining pavements | 

## Slide 37: Every year each lane mile on the network ages 1 YEAR
Pavement Management
Remaining Service Life (RSL) TDOT – 37,000 Lane Miles

## Slide 38: Each type of pavement treatment is expected to add a certain number of years of life to the pavement Expected Life (Years) x Lane Miles = Lane-Mile-Years Added to System
Pavement Management
Remaining Service Life (RSL) TDOT – 37,000 Lane Miles

## Slide 39: RSL Average Life Extension by Treatment
Pavement Treatment Options | Expected Added Pavement Life
Asphalt Overlay (>1.25” (30 mm) | 10-12 years
Ultra Thin Overlay (< 1.25”) | 6-10 years
Micro Surface | 6-8 years
Chip Seal | Up to 6 years
Joint Stabilization | 3 years
Crack Seal | Up to 3 years
Fog Seal | Up to 4 years
Grinding Concrete Pavements | Varies
Cleaning and Resealing Joints Concrete | Varies

## Slide 40
  PQI
  Best Indicator of Overall Pavement Condition
  0 – 5 Scale (5 is best)
Pavement Management System - HPMA
By Using | HPMA Calculates
Roughness (IRI) | Pavement Smoothness Index (PSI)
Distress (Cracking) | Pavement Distress Index (PDI)
PSI & PDI | Pavement Quality Index (PQI)

## Slide 41: Pavement Condition Forecast - Interstate

## Slide 42: Pavement Condition Forecast – State Route

## Slide 43
Pavement Management
  Current funding on state route system not sufficient
  Freight loading expected to increase dramatically over next 25 years
  Increase in materials costs = less paving or higher cost
  Evaluate treatment options
  Improve trade-off analysis for pavement/bridge preservation
  Increase in budget
Challenges
Future Considerations

## Slide 44
MAINTENANCE MANAGEMENT

## Slide 45
Maintenance Management
  Inventory Data collection by HQ
  Asset Condition Assessments Performed by Districts
  MMS managed by HQ
  Daily Work Reporting by Districts
  Budget Prepared by HQ
  Based on Inventory at County/System Level
  Level of Service
Who is Involved?
How are Funds Allocated to Regions/Districts?

## Slide 46
Maintenance Management
  Historical Expenditures by Activity
  Condition Assessment
  Allocation by Inventory
  Maintenance Quality Assurance (MQA)
How is the Program Optimized?
Performance Measures

## Slide 47: Building Maintenance Budgets
Inventory
X
Level of Service
=
Work Quantity
Work Quantity
X
Unit Cost
=
Budget

## Slide 48: Asset Management
Maintenance Management System
Level of Service
Condition Assessment
Asset Inventory
Inventory
Asset Inventory

## Slide 49: Asset Inventory – Data Collection
Mobile LiDAR
Barrier Wall
Pavement Markings
Rumble Strips
Mowing Area
Signs
Automatic & Semi-Automatic
Feature Extraction

## Slide 50: Asset Inventory – GIS Maps
Guardrail & Cable Rail

## Slide 51: Asset Inventory – GIS Maps
Pavement Markings

## Slide 52: Asset Inventory – GIS Maps
Pavement Markings

## Slide 53: Asset Inventory – GIS Maps
Mowing Acres

## Slide 54: Asset Inventory - MMS

## Slide 55: Asset Management
Level of Service
Maintenance Management System
Level of Service
Condition Assessment
Asset Inventory
Level of Service

## Slide 56: Level of Service
Frequency of Performed Maintenance
Example: Mowing Activity
    3 cycles of mowing on all acres on state routes
    Level of Service = 3.000 acres/acre
    4 cycles of mowing on all acres on interstate routes
    Level of Service = 4.000 acres/acre
3 cycles
4 cycles
Level of Service

## Slide 57: Level of Service
Frequency of Performed Maintenance
Example: Sign Sheeting Replacement
    If sign sheeting lasts 10 years,
    Should replace 1/10th of inventory each year
    Level of Service = 0.100 Sq Ft. / Sq. Ft.
Level of Service

## Slide 58: Building Maintenance Budgets
Inventory
X
Level of Service
=
Work Quantity

## Slide 59: Activity Unit Cost
Unit Cost
Inventory

## Slide 60: Building Maintenance Budgets
Inventory
X
Level of Service
=
Work Quantity
X
Unit Cost
=
Budget
Work Quantity

## Slide 61: Asset Management
Maintenance Management System
Level of Service
Condition Assessment
Asset Inventory
Condition Assessment
Condition
Assessment

## Slide 62: Condition Assessment
Maintenance Quality Assurance

## Slide 63: Condition Assessment
  Random Samples
  1/10th mile segments
  Monthly Inspections
  Performed by District Staff
  10% QA/QC by Consultants
Maintenance Quality Assurance

## Slide 64: Condition Assessment
Maintenance Quality Assurance
  Measure Inventory/Deficiency
  6 Elements – Pavement, Shoulder, Roadside, Drainage, Traffic Services, Ramps
  61 Characteristics
  LOS A - F

## Slide 65: Condition Assessment
  Will eventually be tied to budget
  Targets for each characteristic & element group
  Targets can be revised based on available funding
  Use Pavement System data to improve inspector safety
Maintenance Quality Assurance

## Slide 66: Condition Assessment
Maintenance Quality Assurance

## Slide 67: Condition Assessment
Maintenance Quality Assurance
Predict $$ required to move up from LOS C to LOS B
Establish Needs-Based Budgets
If need-based budget not possible, then
Predict LOS to expect based on funding level provided
+ $179,000

## Slide 68
RESULTS

## Slide 69: The Good News
States without Transportation Debt
NE - 9th
WY - 18th
IA - 28th
SD - 39th
TN - 2nd
Notes: The Good News, Tennessee is bucking this trend.
After 10 years of implementing and expanding this strategy, Tennessee’s state highway network is in the best condition it has been since detailed records have been kept.
CNBC rates Tennessee as the second best Transportation Infrastructure in the US.
Overdrive Magazine (A Trucking Industry Periodical) consistently rates Tennessee in the top 5 in the US. And they rate I-40 in Tennessee as the best Interstate segment in the US.
We do all of this while using no debt in the delivery of our projects and programs.

## Slide 70: Pavements - How Does TDOT Compare?
Chart: IRI (International Roughness Index)
| District of Columbia | Hawaii | California | Tennessee | Idaho
Rural Interstates | 128 | 110 | 45 | 45
Urban Interstates | 201 | 147 | 132 | 62 | 50
1st
2nd
49th
50th

## Slide 71: While there are only 8 states with more bridges on the National Highway System than Tennessee, there are 42 states with more structurally deficient bridges2. 2Federal Highway Administration’s (FHWA) 2010 National Bridge Inventory (NBI)
Chart: % Structurally Deficient Bridges on National Highway System by State
| FLORIDA | KANSAS | TEXAS | DELAWARE | NEVADA | GEORGIA | MISSISSIPPI | ARIZONA | SOUTH DAKOTA | TENNESSEE | NEBRASKA | UTAH | MINNESOTA | ARKANSAS | LOUISIANA | NORTH DAKOTA | MONTANA | ALABAMA | WISCONSIN | MARYLAND | OREGON | NEW MEXICO | VIRGINIA | IDAHO | OHIO | MISSOURI | KENTUCKY | WASHINGTON | IOWA | CONNECTICUT | NORTH CAROLINA | INDIANA | VERMONT | COLORADO | ILLINOIS | NEW JERSEY | NEW YORK | HAWAII | SOUTH CAROLINA | MICHIGAN | NEW HAMPSHIRE | MAINE | OKLAHOMA | WEST VIRGINIA | PUERTO RICO | ALASKA | MASSACHUSETTS | WYOMING | CALIFORNIA | DIST. OF COL. | PENNSYLVANIA | RHODE ISLAND
% Structurally Deficient | 0.0044346 | 0.0066445 | 0.007387 | 0.0084746 | 0.0087065 | 0.010963 | 0.012312 | 0.016762 | 0.018428 | 0.021642 | 0.024352 | 0.026596 | 0.026659 | 0.027676 | 0.02853 | 0.030418 | 0.030488 | 0.030649 | 0.032058 | 0.033153 | 0.035256 | 0.037796 | 0.041265 | 0.041444 | 0.04512 | 0.046586 | 0.047215 | 0.047918 | 0.049604 | 0.051592 | 0.052003 | 0.056349 | 0.059448 | 0.061856 | 0.065359 | 0.068173 | 0.068578 | 0.073113 | 0.074855 | 0.076591 | 0.078519 | 0.082789 | 0.08435 | 0.094909 | 0.098684 | 0.098958 | 0.10112 | 0.10947 | 0.12023 | 0.12727 | 0.13117 | 0.20144
Chart: # of Bridges on National Highway System by State
| TEXAS | CALIFORNIA | PENNSYLVANIA | OHIO | FLORIDA | ILLINOIS | NEW YORK | VIRGINIA | TENNESSEE | NORTH CAROLINA | MISSOURI | ALABAMA | OKLAHOMA | WISCONSIN | LOUISIANA | ARIZONA | INDIANA | GEORGIA | MICHIGAN | NEW JERSEY | KANSAS | WASHINGTON | COLORADO | MISSISSIPPI | MASSACHUSETTS | ARKANSAS | IOWA | KENTUCKY | MINNESOTA | CONNECTICUT | NEW MEXICO | OREGON | MARYLAND | SOUTH CAROLINA | MONTANA | WYOMING | NEBRASKA | WEST VIRGINIA | UTAH | SOUTH DAKOTA | NEVADA | IDAHO | NEW HAMPSHIRE | PUERTO RICO | NORTH DAKOTA | VERMONT | MAINE | HAWAII | ALASKA | RHODE ISLAND | DELAWARE | DIST. OF COL.
# NHS Bridges | 14485 | 7569 | 4338 | 4211 | 4059 | 3672 | 3558 | 3320 | 3142 | 2846 | 2812 | 2806 | 2786 | 2745 | 2734 | 2625 | 2591 | 2554 | 2546 | 2523 | 2408 | 2233 | 2231 | 2193 | 2057 | 1915 | 1895 | 1885 | 1688 | 1570 | 1561 | 1560 | 1478 | 1376 | 1312 | 1288 | 1273 | 1159 | 1128 | 814 | 804 | 748 | 675 | 608 | 526 | 471 | 459 | 424 | 384 | 278 | 236 | 110
Bridges - How Does TDOT Compare?

## Slide 72: Questions?
Jerry Hatcher
Jerry.hatcher@tn.gov
615-741-2027