## Slide 1: NCHRP Domestic Scan 14-01: Leading Management Practices for Determining Funding Levels for Maintenance and Preservation
Using Data to Evaluate Funding Needs and Allocate Funding

## Slide 2: Level of Service [LOS] Analysis
Asset Inventory How much do I have?
Condition/MQA Data What shape is it in?
Work Reporting How much have I worked on it?
It all starts with an analysis…

## Slide 3
Most expenditures are captured and analyzed through Level of Service (LOS)
  Excludes Salaries, Cyclical, Contractual and Historical expenditures
Inventories are either actual or extrapolated amounts for a given District and county.
More Accurate More Accurate
Inventories Outputs
ASSET INVENTORIES
=

## Slide 4: CURRENT CONDITION
PMS
Work
Reporting
MQA
BrM
AMMO

## Slide 5
Labor – Average wage rate per position used
Equipment – Actual rental rates for equipment used in an operation.
Materials – Real costs of materials used.
All Costs to maintain the current LOS are captured for a County and Route.
WORK REPORTING

## Slide 6
LOS ANALYSIS EXAMPLE
Inventory = 10,000 LF
Work Reported (Activity 551) = 1,000 LF
Current LOS = C
Target LOS = B
Guard Rail:

## Slide 7
LOS ANALYSIS EXAMPLE
Reported Work Qty / Inventory Qty * 100 = Current Work Quantity
(1,000 /10,000)*100 = 10%
i.e Worked on 10% of the system

## Slide 8
LOS ANALYSIS EXAMPLE
Current LOS – Target LOS = Increased Level of Effort (LOE)
4% - 2% = 2%

## Slide 9
LOS ANALYSIS EXAMPLE
Increased LOE + Existing LOE = Needed LOE
10% + 2% = 12%
Needed LOE x Inventory Qty = LOE Work Qty
0.12 x 10,000 LF = 1,200 LF
LOE Work Qty / ADP = Annual Crew Days
1,200 LF / 50 LF/Day = 24 Crew Days

## Slide 10
LOS ANALYSIS EXAMPLE
Labor Cost = Crew Days x Crew Size x Hours per day x Avg Labor Hour Rate
Equipment Cost = Crew Days x Hours per Day x Equipment Hourly Rate
Material Cost = Crew Days x Qty per Crew Day x Material

## Slide 11
Needs-based budget is calculated for each District at the end of the year.
Calculated from current LOS at the current LOE and computes the need to reach the Target LOS for all items
Historical & Contractual amounts are added to Work Plan.
Plans are rolled into a State-wide Cumulative Budget.
LOS ANALYSIS & WORK PLAN

## Slide 12
FUNDING DISTRIBUTION

## Slide 13
OVERLAY DISTRIBUTION
ROUTINE MAINTENANCE DISTRIBUTION
FUNDING DISTRIBUTION

## Slide 14
OVERLAY DISTRIBUTION
ROUTINE MAINTENANCE DISTRIBUTION
FUNDING DISTRIBUTION
TOUGH TO RECONCIL FIXED, HISTORICAL COSTS

## Slide 15
FUNDING DISTRIBUTION
ELEMENT / ACTIVITY
COMMODITY / CONTRACT

## Slide 16
FUNDING DISTRIBUTION
Continue to stress the use of work plan outputs for planning work in the District.
Begin a gradual shift towards the Needs- Based distribution.
Develop a weighed priority system focused on safety

## Slide 17
Heath T. Patterson, P.E.
MDOT State Maintenance Engineer & Emergency Coordinating Officer
hpatterson@mdot.ms.gov
601-359-7113